Problem 1
Consider the discrete-time signal given by:
x(n) = lbrace -1, -2, 0, 1, 1, 1, 0, 0 rbrace

Sketch and label carefully each of the following signals:
1. x(n - 5)
2. 3x(n + 2)
3. x(-n-7)
4. x(n)u(n)
Solution:

n	0	1	2	3	4	5	6	7	8	9	10
x(n)	0	0	0	-1	-2	0	1	1	1	0	0

x(n-5) = lbrace 0, 0, 0, -1, -2, 0, 1, 1, 1, 0, 0 rbrace

n	-4	-3	-2	-1	0	1	2	3
x(n)	-3	-6	0	3	3	3	0	0

3x(n+2) = lbrace -3, -6, 0, 3, 3, 3, 0, 0 rbrace

n	-12	-11	-10	-9	-8	-7	-6	-5	-4	-3	-2	-1	0
x(n)	0	0	1	1	1	0	-2	-1	0	0	0	0	0

x(-n - 7) = x(-(n + 7)) = lbrace 0, 0, 1, 1, 1, 0, -2, -1, 0, 0, 0, 0, 0 rbrace

n	-2	-1	0	1	2	3	4	5
x(n)	0	0	0	1	1	1	0	0

x(n)u(n) = lbrace 0, 0, 0, 1, 1, 1, 0, 0 rbrace

Problem 2
Represent the system given by the following input-output equation as a block-diagram:
y(n) = x(n - 2) + 2x(n - 3) + x^{2}(n - 2) + y(n - 5)
Solution:

Problem 3
For each variant of the following systems, determine whether it is static or dynamic, time variant or time invariant, linear or non-linear, and causal or non-causal. Justify your answer:
1. y(n) = x(n - 7) + 2x(n - 3)
2. y(n) = (n + 1)x(n)
3. y(n) = cos(x(n)) + x(n - 3)
Solution:
1. The system is dynamic because its output at any instant n depends on past samples of the input. y(n, k) = x(n – k – 7) + 2x(n – k - 3) and y(n – k) = x(n – k – 7) + 2x(n – k – 3). Since y(n, k) = y(n - k)→Time invariant. If we input x1(n) to the system, we get y1(n) = x1(n – 7) + 2x1(n – 3). If we input x2(n) to the system, we get y2(n) = x2(n – 7) + 2x2(n – 3). If we input a1x1(n) + a2x2(n) to the system we get y3(n) = a1(x1(n – 7) + 2x1(n – 3)) + a2(x2(n – 7) + 2x2(n – 3)). If we add a1y1(n) and a2y2(n), we get a1y1(n) + a2y2(n) = a1(x1(n – 7) + 2x1(n – 3)) + a2(x2(n – 7) + 2x2(n – 3)). Since y3(n) = a1y1(n) + a2y2(n), then the system is linear. The system is causal because its output at any time point depends only on past inputs.
2. The system is static because its output at any instant n depends at most on the input sample at the same time. y(n, k) = (n + 1)x(n – k) and y(n – k) = (n – k + 1)x(n – k). Since y(n, k) ≠ y(n - k)→Time invariant. If we input x1(n) to the system, we get y1(n) = (n + 1)x1(n). If we input x2(n) to the system, we get y2(n) = (n + 1)x2(n). If we input a1x1(n) + a2x2(n) to the system we get y3(n) = a1((n + 1)x1(n)) + a2((n + 1)x2(n)). If we add a1y1(n) and a2y2(n), we get a1y1(n) + a2y2(n) = a1((n + 1)x1(n)) + a2((n + 1)x2(n)). Since y3(n) = a1y1(n) + a2y2(n), then the system is linear. The system is non-causal because its output at any time point depends on future inputs.
3. The system is dynamic because its output at any instant n depends on past samples of the input. y(n, k) = cos(x(n – k)) + x(n – k – 3) and y(n – k) = cos(x(n – k)) + x(n – k – 3). Since y(n, k) = y(n – k)→Time invariant. If we input x1(n) to the system, we get y1(n) = cos(x1(n)) + x1(n - 3). If we input x2(n) to the system, we get y2(n) = cos(x2(n)) + x2(n - 3). If we input a1x1(n) + a2x2(n) to the system we get y3(n) = cos(a1x1(n)) + a1x1(n - 3) + cos(a2x2(n)) + a2x2(n - 3). If we add a1y1(n) and a2y2(n), we get a1y1(n) + a2y2(n) = a1cos(x1(n)) + a1x1(n - 3) + a2cos(x2(n)) + a2x2(n – 3). Since y3(n) ≠ a1y1(n) + a2y2(n), then the system is non-linear. The system is causal because its output at any time point depends only on past inputs.

Problem 4
Implement the following functions using MATLAB or Python:
- Downsample: A function that takes as input the file name of an input audio file, the downsampling factor (integer only), and the file name of the output downsampled file. This function should change the sampling rate of the input audio from FS to (FS /downsampling factor) without changing the duration of the audio.
- IncreaseSpeed: A function that takes as input the file name of an input audio file, the speeding factor (integer only), and the file name of the output increased speed audio file. This function should change the duration of the input audio from T to (T/speeding factor) without changing the sampling rate.
Deliverables:
- Your code (either MATLAB .m files or Python .py or Jupyter notebook files).
- Apply the Downsample function to the audio file provided “Audio1.wav” using downsampling factor of 2, 3, and 10. Name the output files “Audio1_Down_2.wav”, “Audio1_Down_3.wav”, and “Audio_Down_10.wav”, respectively. The sampling rate of the original audio is 14.4kHz.
- The file “Audio1.wav” represents the following signal:
  x_{a}(t) = 0.1sin(2 %pi times 1000t) + 0.9sin(2%pi times 3000t + {%pi} over {3})
  Comment on which of the downsampling factors results in a noticeable change in the audio and the reasons for such a change.
- Apply the Downsample function to the audio file provided “Audio2.wav” using a downsampling factor of 2, 10, and 35. Name the output files “Audio2_Down_2.wav”, “Audio2_Down_10.wav”, and “Audio2_Down_35.wav”, respectively. The sampling rate of the original audio is 44.1kHz.
- Comment on the quality of the audio obtained after downsampling the file “Audio2.wav”.
- Apply the IncreaseSpeed function to the audio file provided “Audio1.wav” using a speeding factor of 2, 3, and 4. Name the output files “Audio1_Inc_2.wav”, “Audio1_Inc_3.wav”, and “Audio1_Inc_4.wav”, respectively.
- Apply the IncreaseSpeed function to the audio file provided “Audio2.wav” using a speeding factor of 2, 3, and 4. Name the output files “Audio2_Inc_2.wav”, “Audio2_Inc_3.wav”, and “Audio2_Inc_4.wav”, respectively.
Solution:
x_{a}(nT) = x(n)
Using a downsampling factor of 2, we get
x_{2}(n) = 0.1sin({5 %pi} over {18}n) + 0.9sin({5 %pi} over {6}n + {%pi} over {3})
Using a downsampling factor of 4, we get
x_{4}(n) = 0.1sin({5 %pi} over {12}n) + 0.9sin({5 %pi} over {4}n + {%pi} over {3})
Mapping ɷ to be in the range -π ≤ ɷ ≤ π
{5%pi} over {4} - 2%pi ={-3%pi} over {4}
x_{10}(n) = 0.1sin({5 %pi} over {12}n) + 0.9sin({-3%pi} over {4}n + {%pi} over {3})
Using a downsampling factor of 10, we get
x_{10}(n) = 0.1sin({25 %pi} over {18}n) + 0.9sin({25 %pi} over {6}n + {%pi} over {3})
Mapping each ɷ to be in the range -π ≤ ɷ ≤ π
{25%pi} over {18} - 2%pi ={-11%pi} over {18}
{25%pi} over {6} - 2%pi ={%pi} over {6}
x_{10}(n) = 0.1sin({-11 %pi} over {18}n) + 0.9sin({%pi} over {6}n + {%pi} over {3})
The Sampling Theorem
If the highest frequency contained in an analog signal xa(t) is Fmax and the signal is sampled at a rate FS > 2Fmax, then xa(t) can be exactly recovered from its sample values
The sampling rate FN = 2Fmax is called the Nyquist rate
The frequencies present in the signal are F1 = 1000 Hz and F2 = 3000 Hz
Thus, Fmax = 3000 Hz
The Nyquist rate is then 3000 × 2 = 6000 Hz
The downsampling factors that result in a noticeable change in the audio are 4 and 10. The reasons for such a change is that dividing the sampling frequency of 14.4 kHz by 4 results in a sampling frequency of 4.8 kHz. 4.8 kHz is less than twice the highest frequency in the audio. Similarly, dividing the sampling frequency of 14.4 kHz by 10 results in a sampling frequency of 1.44 kHz. This frequency is much less than twice the highest frequency in the audio.
The quality of the audio obtained after downsampling the file “Audio2.wav” dramatically decreased.
Important Notes:
- All deliverables should be included in one .zip file.
- For Problems 1, 2, and 3, write your answers in a Word or PDF file and include it in the .zip file.
- For Problem 4, you need to implement the downsampling and increasing speed from scratch. Don’t use ready made functions that you might find available in MATLAB or Python.
- This is an individual assignment.